## Slide 1: Low-Level Programming Overview
Language-defined Context
Querying Representation Choices
Specifying Representation
Interrupt Handling

## Slide 2: Just An Overview
There is far too much to cover in the time available
  Usually this is a few hundred slides
Therefore we highlight the facilities and use examples to illustrate them
  Real code taken from the Ada Drivers Library
    We show a slightly earlier version for illustration
  https://github.com/AdaCore/Ada_Drivers_Library
  https://github.com/AdaCore/Ada_Drivers_Library/tree/master/arch/ARM/STM32/driver_demos
Some good Ada books are available on this topic

## Slide 3: Agenda
Language-defined Context
Querying Representation Choices
Specifying Representation
Interrupt Handling
Concluding Remarks

## Slide 4: The Package “System”
Contains implementation-dependent values & definitions
The type Address
Numeric limits
Priorities, normal and interrupt level
Definition of default bit order
  So-called “endianness”
System-wide restrictions
Others…

## Slide 5: The Type Address
Is implementation-defined
RM suggests a private type due to hardware differences
  A strong recommendation
Write your code accordingly for portability
  Even if a given implementation doesn’t follow the suggestion
Relational operators are defined
Address arithmetic is defined elsewhere
  Package System.Storage_Elements (shown momentarily)

## Slide 6: Addressing
Addresses refer to “storage units”
  Smallest machine-addressable entity
Predefined constant Null_Address supplied
Size of storage unit defined as a named number
  Expressed in terms of bits (e.g., 8)
  Name is Storage_Unit
Size of machine “word” defined as named number
  Expressed in terms of bits (e.g., 32, or 64, or …)
  Name is Word_Size
Storage_Unit : constant := 8;
Word_Size : constant := 32;

## Slide 7: Priorities
Full range defined by type Any_Priority
  Others are subtypes
Normal range for tasks & protected objects
  The subtype “Priority”
Priorities that mask interrupts
  The subtype “Interrupt_Priority”
Default value
Any_Priority
Priority
Any_Priority'Last
N+1
…
N
Any_Priority'First
…
Default_Priority
…
Interrupt_Priority
Urgency

## Slide 8: Bit Ordering
Defined by type
Default defined by a static constant of that type
type Bit_Order is (High_Order_First, Low_Order_First);
High-Order Bits
Low-Order Bits
0
31
Big-Endian: High order bit is in bit zero
Little-Endian: Low order bit is in bit zero
31
0
High_Order_First
Low_Order_First
Default_Bit_Order : constant Bit_Order := implementation-defined-value;
Notes: “First” corresponds to bit 0

## Slide 9: Agenda
Language-defined Context
Querying Representation Choices
Specifying Representation
Interrupt Handling
Concluding Remarks

## Slide 10: Most Common Representation Queries
X'Address
  Value is in terms of System.Address
  For program units, the address of the code
  For variables, where stored
X'Size
  In terms of bits
  For objects, actual number used to hold the object
  For discrete types, minimum number to represent values
    Signed and modular integer types
    Enumeration types
Others are possible but less used
  Record components’ locations within a record
  Bit order, etc.

## Slide 11: Object Size versus Type Size
Object size may be larger than type size
  Due to hardware considerations
  Performance
A : Natural;
B : Boolean;
C : Integer;
Boolean'Size = 1 on all machines
B'Size = 8 (typically)
B
C
C
C
C
A
A
A
A
Natural'Size = 31 (on a 32-bit machine)
A'Size = 32 (on a 32-bit machine)
subtype Natural is Integer range 0 .. Integer'Last;
C'Size = Integer'Size = 32 (on a 32-bit machine)
Notes: Boolean'Size = 1 by RM 13.3(49)

## Slide 12: Agenda
Language-defined Context
Querying Representation Choices
Specifying Representation
Interrupt Handling
Concluding Remarks

## Slide 13: Specifying Representation Facilities
Size of objects of given type
Alignment for types
Enumeration value encoding
Array component sizes
Physical layout for record types
Locations (addresses) for code and data objects
Others…
Can be rejected if impossible

## Slide 14: Address Literals and Arithmetic
RM recommends type Address be private so need facilities for specifying literals
package System.Storage_Elements is
type Storage_Offset is range implementation-defined;
...
function "+" (Left : Address; Right : Storage_Offset) return Address;
function "-" (Left : Address; Right : Storage_Offset) return Address;
function "-" (Left, Right : Address) return Storage_Offset;
...
type Integer_Address is implementation-defined;
function To_Address (Value : Integer_Address) return Address;
function To_Integer (Value : Address) return Integer_Address;
...
end System.Storage_Elements;
Modular or signed
Arithmetic
“Constructors”
Signed
Notes: The Transputer used signed addresses and documents them as such. Positive addresses were used for application code, negative for operating system code.

## Slide 15: Specifying An Entity’s Address
For program units and data
  For program units, placement of first machine instruction
Syntax
  Expression is of type System.Address
Use to overlay data objects is legal & questionable
  Consider unchecked conversion (handles alignment issue too)
for identifier 'Address use expression;
X : Bits32;
Y : Integer;
for Y'Address use X'Address;
Object : My_Type with
Address => expression;
Ada 2012

## Slide 16: Dynamically Converting Addresses
More flexible than memory-mapped variables
  Types "viewed" by conversion can change
Generic package defined in the Core language
  NB: cannot work in all cases!
generic
type Object (<>) is limited private;
package System.Address_To_Access_Conversions is
type Object_Pointer is access all Object;
function To_Pointer (Value : Address) return Object_Pointer;
function To_Address (Value : Object_Pointer) return Address;
pragma Convention (Intrinsic, To_Pointer);
pragma Convention (Intrinsic, To_Address);
end System.Address_To_Access_Conversions;

## Slide 17: Dynamic Address Conversion Example
with Interfaces;
with System.Address_To_Access_Conversions;
package body Byte_Swapping is
type Word is new Interfaces.Unsigned_16;
package Word_Ops is new System.Address_To_Access_Conversions (Word);
use Word_Ops;
procedure Swap2 (Location : in System.Address) is
X : Word renames To_Pointer(Location).all;
begin
X := Shift_Left (X, 8) or Shift_Right (X, 8);
end Swap2;
…
end Byte_Swapping;
Memory
(bytes)

## Slide 18: Aspects for Shared/Memory-Mapped Variables
Aspect/pragma “Independent”
  Ensures entity is independently addressable
Aspect/pragma “Volatile”
  Roughly, ensures all reads/writes are effective
Aspect/pragma “Atomic”
  Loads and stores must be indivisible
  Every atomic type or object is also volatile
Aspect/pragma “Volatile_Full_Access”
  Roughly, like Atomic but ensures whole object is loaded or stored even if only components are accessed
  Defined by GNAT

## Slide 19: Extended Example: Arm GPIO
General Purpose I/O on Arm devices
  A combination of a port and multiple dedicated pins
  MCUs will offer several such ports
Ports are memory-mapped devices located on MCUs at device-specific addresses
We use an abstract data type to represent any GPIO port/pin object
We declare as many such objects as the device provides
We use address clauses to place each object at its dedicated address

## Slide 20
package STM32F4.GPIO is
type GPIO_Port is limited private;
…
type GPIO_Pin is (Pin_0, Pin_1, Pin_2, …, Pin_14, Pin_15);
type GPIO_Point is record
Port : access GPIO_Port;
Pin : GPIO_Pin;
end record;
…
function Set (This : GPIO_Point) return Boolean with Inline;
procedure Set (This : GPIO_Point) with Inline;
procedure Clear (This : GPIO_Point) with Inline;
…
procedure Lock (Point : GPIO_Point);
…
private
…
type GPIO_Port is limited record …
for GPIO_Port use record …
end STM32F4.GPIO;

## Slide 21: Declaring Memory-Mapped Devices (1)
with System.Storage_Elements;
use System;
use type System.Storage_Elements.Storage_Offset;
package STM32F4 is
Peripheral_Base : constant Address := System'To_Address (16#4000_0000#);
APB1_Peripheral_Base : constant Address := Peripheral_Base;
APB2_Peripheral_Base : constant Address := Peripheral_Base + 16#0001_0000#;
AHB1_Peripheral_Base : constant Address := Peripheral_Base + 16#0002_0000#;
AHB2_Peripheral_Base : constant Address := Peripheral_Base + 16#1000_0000#;
GPIOA_Base : constant Address := AHB1_Peripheral_Base + 16#0000#;
GPIOB_Base : constant Address := AHB1_Peripheral_Base + 16#0400#;
GPIOC_Base : constant Address := AHB1_Peripheral_Base + 16#0800#;
…
ADC1_Base : constant Address := APB2_Peripheral_Base + 16#2000#;
…

## Slide 22: Declaring Memory-Mapped Devices (2)
with System; use System;
with STM32F4.GPIO; use STM32F4.GPIO;
with STM32F4.DMA; use STM32F4.DMA;
…
use STM32F4; -- for base addresses
package STM32F4xxx is
…
GPIO_A : aliased GPIO_Port with Volatile, Address => GPIOA_Base;
GPIO_B : aliased GPIO_Port with Volatile, Address => GPIOB_Base;
GPIO_C : aliased GPIO_Port with Volatile, Address => GPIOC_Base;
…
ADC_1 : aliased Analog_To_Digital_Converter with Volatile, Address => ADC1_Base;
…
Memory-mapped devices…
… at these addresses

## Slide 23
package STM32F4.GPIO is
…
type GPIO_Pin is
(Pin_0, Pin_1, Pin_2, Pin_3, Pin_4, Pin_5, Pin_6, Pin_7,
Pin_8, Pin_9, Pin_10, Pin_11, Pin_12, Pin_13, Pin_14, Pin_15);
for GPIO_Pin use
(Pin_0 => 16#0001#,
Pin_1 => 16#0002#,
Pin_2 => 16#0004#,
Pin_3 => 16#0008#,
Pin_4 => 16#0010#,
Pin_5 => 16#0020#,
Pin_6 => 16#0040#,
Pin_7 => 16#0080#,
Pin_8 => 16#0100#,
Pin_9 => 16#0200#,
Pin_10 => 16#0400#,
Pin_11 => 16#0800#,
Pin_12 => 16#1000#,
Pin_13 => 16#2000#,
Pin_14 => 16#4000#,
Pin_15 => 16#8000#);
for GPIO_Pin'Size use 16; -- confirming
Notes: Example for specifying representation of an enumeration type.

## Slide 24
package STM32F4.GPIO is
…
type Pin_IO_Modes is (Mode_In, Mode_Out, Mode_AF, Mode_Analog);
type Pin_Output_Types is (Push_Pull, Open_Drain);
type Pin_Output_Speeds is
(Speed_2MHz, Speed_25MHz, Speed_50MHz, Speed_100MHz);
type Internal_Pin_Resistors is (Floating, Pull_Up, Pull_Down);
private
type Pin_Modes_Register is array (0 .. 15) of Pin_IO_Modes with
Component_Size => Pin_IO_Modes'Size;
type Output_Types_Register is array (0 .. 15) of Pin_Output_Types with
Component_Size => Pin_Output_Types'Size;
type Output_Speeds_Register is array (0 .. 15) of Pin_Output_Speeds with
Component_Size => Pin_Output_Speeds'Size;
type Resistors_Register is array (0 .. 15) of Internal_Pin_Resistors with
Component_Size => Internal_Pin_Resistors'Size;
…
end STM32F4.GPIO;
Notes: Example for specifying component size of an array type.

## Slide 25
…
private
…
type GPIO_Port is limited record
MODER : Pin_Modes_Register;
OTYPER : Output_Types_Register;
Reserved_1 : Half_Word;
OSPEEDR : Output_Speeds_Register;
PUPDR : Resistors_Register;
IDR : Half_Word; -- input data register
Reserved_2 : Half_Word;
ODR : Half_Word; -- output data register
Reserved_3 : Half_Word;
BSRR_Set : Half_Word; -- bit set register
BSRR_Reset : Half_Word; -- bit reset register
LCKR : Word;
AFR : Bits_16x4; -- alternate function registers
Reserved_4 : Reserved_246x32;
end record with
Volatile_Full_Access,
Size => 16#400# * 8;
for GPIO_Port use record …
end STM32F4.GPIO;
Notes: Example for specifying representation of a record type, i.e., VFA and size expected.

## Slide 26
type GPIO_Port is limited record
MODER : Pin_Modes_Register;
OTYPER : Output_Types_Register;
Reserved_1 : Half_Word;
OSPEEDR : Output_Speeds_Register;
PUPDR : Resistors_Register;
IDR : Half_Word;
Reserved_2 : Half_Word;
ODR : Half_Word;
Reserved_3 : Half_Word;
BSRR_Set : Half_Word;
BSRR_Reset : Half_Word;
LCKR : Word;
AFR : Bits_16x4;
Reserved_4 : Reserved_246x32;
end record with
Volatile_Full_Access,
Size => 16#400# * 8;
for GPIO_Port use record
MODER at 0 range 0 .. 31;
OTYPER at 4 range 0 .. 15;
Reserved_1 at 6 range 0 .. 15;
OSPEEDR at 8 range 0 .. 31;
PUPDR at 12 range 0 .. 31;
IDR at 16 range 0 .. 15;
Reserved_2 at 18 range 0 .. 15;
ODR at 20 range 0 .. 15;
Reserved_3 at 22 range 0 .. 15;
BSRR_Set at 24 range 0 .. 15;
BSRR_Reset at 26 range 0 .. 15;
LCKR at 28 range 0 .. 31;
AFR at 32 range 0 .. 63;
Reserved_4 at 40 range 0 .. 7871;
end record;
Notes: Example for specifying representation of a record type components’ layout.

## Slide 27
with STM32F4.RCC;
with STM32F4.SYSCFG;
with System.Machine_Code;
package body STM32F4.GPIO is
function Set (This : GPIO_Point) return Boolean is
Pin_Mask : constant Half_Word := GPIO_Pin'Enum_Rep (This.Pin);
begin
return (This.Port.IDR and Pin_Mask) = Pin_Mask;
end Set;
procedure Set (This : GPIO_Point) is
begin
This.Port.BSRR_Set := GPIO_Pin'Enum_Rep (This.Pin);
end Set;
…
function Current_Output (Port : GPIO_Port) return Half_Word is
begin
return Port.ODR;
end Current_Output;
procedure Write_Output (Port : in out GPIO_Port; Data : Half_Word) is
begin
Port.ODR := Data;
end Write_Output;
end STM32F4.GPIO;
Notes: Example access to record components, remains in high level.

## Slide 28
package STM32F4.GPIO is
…
procedure Lock (Point : GPIO_Point);
…
private
…
LCCK : constant Word := 16#0001_0000#;
-- As per the Reference Manual (RM0090; Doc ID 018909 Rev 6) pg 282,
-- this is the "Lock Key" used to control the locking of port/pin
-- configurations. It is bit 16 in the lock register (LCKR) of any
-- given port, thus the first bit of the upper 16 bits of the word.
end STM32F4.GPIO;
Notes: Constant used by Lock routine.

## Slide 29
procedure Lock_The_Pin (Port : in out GPIO_Port; Pin : GPIO_Pin) is
Temp : Word with Volatile;
use System.Machine_Code, ASCII;
begin
-- As per the Reference Manual (RM0090; Doc ID 018909 Rev 6) pg 282,
-- a specific sequence is required to set the Lock bit. Throughout the
-- sequence the same value for the lower 15 bits of the word must be
-- used (ie the pin number). The lock bit is referred to as LCKK in
-- the doc.
-- This is the required algorithm:
-- Temp := LCCK or Pin'Enum_Rep;
-- -- set the lock bit
-- Port.LCKR := Temp;
-- -- clear the lock bit
-- Port.LCKR := Pin'Enum_Rep;
-- -- set the lock bit again
-- Port.LCKR := Temp;
-- -- read the lock bit
-- Temp := Port.LCKR;
-- -- read the lock bit again
-- Temp := Port.LCKR;
…
end Lock_The_Pin;
Notes: Example showing assembly language insert.

## Slide 30
procedure Lock_The_Pin (Port : in out GPIO_Port; Pin : GPIO_Pin) is
Temp : Word with Volatile;
use System.Machine_Code, ASCII;
begin
…
-- We use the following assembly language sequence because the above
-- high-level version in Ada works only if the optimizer is enabled.
-- This is not an issue specific to Ada. If you need a specific sequence
-- of instructions you should really specify those instructions.
Asm ("orr r3, %2, #65536" & LF & HT &
"str r3, %0" & LF & HT &
"ldr r3, %0" & LF & HT & -- temp <- pin or LCCK
"str r3, [%1, #28]" & LF & HT & -- temp -> lckr
"str %2, [%1, #28]" & LF & HT & -- pin -> lckr
"ldr r3, %0" & LF & HT &
"str r3, [%1, #28]" & LF & HT & -- temp -> lckr
"ldr r3, [%1, #28]" & LF & HT &
"str r3, %0" & LF & HT & -- temp <- lckr
"ldr r3, [%1, #28]" & LF & HT &
"str r3, %0" & LF & HT, -- temp <- lckr
Inputs => (Address'Asm_Input ("r", Port'Address), -- %1
(GPIO_Pin'Asm_Input ("r", Pin))), -- %2
Outputs => (Word'Asm_Output ("=m", Temp)), -- %0
Volatile => True,
Clobber => ("r2, r3"));
end Lock_The_Pin;
Notes: Example showing assembly language insert. Noe that %1 and %2 are input parameter references for Port and Pin, and %0 is the output reference for Temp. Outputs are always assigned numbers first, hence the %0. We just switched the order of the attributes to show the inputs first.

## Slide 31: Agenda
Language-defined Context
Querying Representation Choices
Specifying Representation
Interrupt Handling
Concluding Remarks

## Slide 32: SP Annex Supports Canonical Model
Defines specific support for managing interrupts
  Package Ada.Interrupts
  Package Ada.Interrupts.Names
Handlers are parameterless protected procedures
  Exported by library-level protected objects (PO’s)
  Defines pragmas to associate handlers to interrupts
Exceptions are not propagated from handlers

## Slide 33: Why Protected Procedure Handlers
Regular procedures have no priority
  Can not integrate with scheduling model
Regular procedures allow race conditions
  E.g., when other code reads values modified by handler
  Interrupts occur asynchronously with application code
Protected objects preclude race conditions
  Application code cannot access data while handler executes
  No new interrupt will be received for same protected object
Relationship of handlers is clearer
  Related handlers are declared within same protected object

## Slide 34: Package Ada.Interrupts
with System;
package Ada.Interrupts is
type Interrupt_Id is <implementation-defined>; -- a discrete or access type
type Parameterless_Handler is access protected procedure;
function Is_Reserved (Interrupt : Interrupt_Id) return Boolean;
function Is_Attached (Interrupt : Interrupt_Id) return Boolean;
function Current_Handler (Interrupt : Interrupt_Id) return Parameterless_Handler;
procedure Attach_Handler (New_Handler : Parameterless_Handler; Interrupt : Interrupt_Id);
procedure Exchange_Handler( Old_Handler : out Parameterless_Handler;
New_Handler : in Parameterless_Handler;
Interrupt : in Interrupt_Id);
procedure Detach_Handler (Interrupt : Interrupt_Id);
function Reference (Interrupt : Interrupt_Id) return System.Address;
private
...
end Ada.Interrupts;

## Slide 35: Package Ada.Interrupts.Names
Specific content is defined by target
Sample for a specific Cortex M4F target
package Ada.Interrupts.Names is
<implementation-defined> : constant Interrupt_Id := <implementation-defined>;
...
end Ada.Interrupts.Names;
package Ada.Interrupts.Names is
Sys_Tick_Interrupt : constant Interrupt_ID := 1;
…
EXTI0_Interrupt : constant Interrupt_ID := 8;
...
DMA1_Stream0_Interrupt : constant Interrupt_ID := 13;
…
ADC_Interrupt : constant Interrupt_ID := 20
…
end Ada.Interrupts.Names;

## Slide 36: ADC Interrupt Handler Example Spec
with Ada.Interrupts.Names;
with Ada.Synchronous_Task_Control; use Ada.Synchronous_Task_Control;
package ADC_Interrupt_Handling is
Regular_Channel_EOC : Suspension_Object;
protected Handler is
pragma Interrupt_Priority;
private
procedure IRQ_Handler with
Attach_Handler => Ada.Interrupts.Names.ADC_Interrupt;
end Handler;
end ADC_Interrupt_Handling;

## Slide 37: ADC Example Architecture
Handler
Procedure
ADC Interrupt
Interrupt Vectors
User
Suspension_Object
Protected Object
ADC
Device

## Slide 38: ADC Interrupt Handler Example Body
with STM32.Device; use STM32.Device;
with STM32.ADC; use STM32.ADC;
package body ADC_Interrupt_Handling is
protected body Handler is
procedure IRQ_Handler is
begin
if Status (ADC_1, Regular_Channel_Conversion_Complete) then
if Interrupt_Enabled (ADC_1, Regular_Channel_Conversion_Complete) then
Clear_Interrupt_Pending (ADC_1, Regular_Channel_Conversion_Complete);
Set_True (Regular_Channel_EOC);
end if;
end if;
end IRQ_Handler;
end Handler;
end ADC_Interrupt_Handling;

## Slide 39: Agenda
Language-defined Context
Querying Representation Choices
Specifying Representation
Interrupt Handling
Concluding Remarks

## Slide 40: Concluding Remarks
Low-level programming is still relatively high level
  “Separation Principle” almost always applies
  Can continue using good software engineering practices
Extensive representation control is available
  As powerful as any high-level language
Various interrupt handling idioms are used
SPARK adds some additional capabilities
We’ve only provided an quick overview…