## Slide 1
GNAT Pro Compiler Extensions

## Slide 2
Vectorization

## Slide 3: Vectorization Principles
Certain architectures offer specialized vectorization instructions
  x86 and SSE
  PowerPC and Altivec
Certain patterns of loops over arrays can be largely optimized with new CPUs and sets of instructions
GCC knows how to take advantage of it in case of “C-like” arrays
Ada unconstrained arrays are very different from C arrays – they could not be vectorized

## Slide 4: Vectorization example
Prior to GNAT Pro 7.1
After GNAT Pro 7.1
type Vector is array (Integer range 1 .. 1_000_000) of Float; procedure Combine (V1, V2 : Vector; R : out Vector) is begin for I in V1'Range loop R (I) := V1 (I) / V2 (I); end loop; end;
type Vector is array (Integer range <>) of Float; procedure Combine (V1, V2 : Vector; R : out Vector) is begin for I in V1'Range loop R (I) := V1 (I) / V2 (I); end loop; end;
-03 | -03 -msse2
33 ms | 10 ms
-03 | -03 -msse2
35 ms | 11 ms

## Slide 5
Lock-Free Protected Types

## Slide 6: Implementing an Atomic Operation
A := A + 1;
[system call lock] [read A in $1] [add 1 in $1] [write $1 in A] [system call unlock]
[loop] [read A in $1] [copy $1 in $old] [add 1 in $1] [if A = $old then write $1 in A else error] [exit when not error] [unlock]

## Slide 7: Usage Example
Lock_Free => False | Lock_Free => True
41 ms | 12 ms
Test on a Windows dual core machine, 200_000 updates done by 2 tasks
protected Counter with Lock_Free => True is procedure Add; private V : Integer := 0; end Counter; protected body Counter is procedure Add is begin V := V + 1; if V = 100 then V := 0; end if; end Add; end Counter;

## Slide 8: Main Restrictions on Lock_Free bodies
Non elementary out parameter
No loop, goto or subprogram call
No reference to more than one protected variable
No side effect
Workaround possible with manual use of System.Atomic_Primitives

## Slide 9
Physical Dimensions

## Slide 10: Problem
Ada offers a nice type system ensuring type consistency
But this type system fails at properly expressing physical dimension
Defining manually all the operators is cumbersome and error-prone
type Length is new Float; type Area is new Float; V1 : Length := 10.0; V2 : Area; begin V1 := V1 * V1; -- Shouldn’t be Length * Length an Area? V2 := V1 * V1; -- Refused at compile time

## Slide 11: The Package System.Dim.Mks
System.Dim.Mks declares a dimension system
Subtype can then be declared to represent simple dimensions
… or more complex ones
with associated constants
type Mks_Type is new Long_Long_Float with Dimension_System => ( (Unit_Name => Meter, Unit_Symbol => 'm', Dim_Symbol => 'L'), (Unit_Name => Kilogram, Unit_Symbol => "kg", Dim_Symbol => 'M'), (Unit_Name => Second, Unit_Symbol => 's', Dim_Symbol => 'T'), (Unit_Name => Ampere, Unit_Symbol => 'A', Dim_Symbol => 'I'), (Unit_Name => Kelvin, Unit_Symbol => 'K', Dim_Symbol => "Î˜"), (Unit_Name => Mole, Unit_Symbol => "mol", Dim_Symbol => 'N'), (Unit_Name => Candela, Unit_Symbol => "cd", Dim_Symbol => 'J'));
subtype Length is Mks_Type with Dimension => (Symbol => 'm', Meter => 1, others => 0);
subtype Speed is Mks_Type with Dimension => (Symbol => 'm/s', Meter => 1, Second => -1, others => 0);
m : constant Length := 1.0; s : constant Second := 1.0; km_h : constant Speed := (1_000.0 * m) / (3_600.0 * s);

## Slide 12: Dimension Checks
The compiler will check dimension consistency
This is a “magic” static check, done by specific compiler work – beyond Ada 2012
h : constant Time := 3600.0 * s; km : constant Length := 1000.0 * m; km_h : constant Speed := km / h; My_Speed : Speed := 50.0 * km_h; My_Time : Time := 5.0 * h; My_Weight : Mass := 300.0 * kg; Distance_Traveled : Length := My_Speed * My_Time; Energy_Needed : Energy := (Distance_Traveled ** 2 * My_Weight) / (My_Time ** 2);

## Slide 13
Endianness Attributes

## Slide 14: Problem
Ada has an extensive set of features to define the memory layout …
… but the endianness of the actual data has to be the one of the target architecture
Portable data representation cross architectures has to be using tricky byte-array representation

## Slide 15: Scalar_Storage_Order
Scalar_Storage_Order can be applied on a composite type (array, record)
It forces the endianness to be of a certain kind
The compiler will automatically insert bitwise transformations on read / write operations if required
The same data structure can have subcomponents with a different endianness if needed

## Slide 16: Scalar_Storage_Order example
Both Scalar_Storage_Order (endianness) and Bit_Order (bit numbering convention) need to be specified on a representation clause
type T is record A, B : Integer; C : Boolean; D : Small_Int; E : Small_Float; F : Color; end record with Bit_Order => High_Order_First, Scalar_Storage_Order => High_Order_First, Size => 128, Alignment => 2; for T use record A at 0 range 0 .. 31; B at 4 range 0 .. 31; C at 8 range 7 .. 7; D at 8 range 0 .. 3; E at 9 range 0 .. 31; F at 13 range 0 .. 2; end record;

## Slide 17
Overflow Checks

## Slide 18: Where are subtype checks performed?
type My_Int is new Integer range -10_000 .. 10_000; V : My_Int := A + C – D;
If A = 9_999, C = 2 and D = 1, what is the result of this expression?
  10_000
  Constraint_Error is raised
  Erroneous (not defined)
Answer: 10_000! Subtype checks are not performed on intermediate results

## Slide 19: How about overflow checks?
If A = Integer’Last, what result of this expression?
  - 1_073_841_824
  1_073_841_824
  Constraint_Error is raised
  Erroneous (not defined)
Answer: depends…
V : Integer := (A + 1) / 2;

## Slide 20: Contract Issues
With contracts, things can get even more problematic
When dealing with a “big” number, the pre condition may be perfectly fine but may raise Constraint_Error because of overflow
Note: there is no subtype check here, only overflow…
procedure P (A, B, C : Integer) with Pre => A ** 2 * B ** 2 > C ** 2;

## Slide 21: GNAT Pro Overflow Policies
All intermediate overflow checked (STRICT)
  Intermediate computations are done in base type
  When checks are enabled, substantial run-time footprint
Most intermediate overflow avoided (MINIMIZED)
  Intermediate computation may be done using a larger base type
  When check are enabled, they're bound to places where absence of overflow can’t be determined
  Smaller footprint with checks, higher reliability of computations
All intermediate overflow avoided (ELIMINATED)
  Uses infinite precision integers when 64 bits computation is not enough
  No need for checks

## Slide 22: How to Select Overflow Policy?
Through the pragma Overflow_Mode
Through the –gnatoxx switch:
  First digit specifies the policy for general expressions
  Second digit specifies the policy for assersion
    1 => STRICT
    2 => MINIMIZED
    3 => ELIMINATED
  Note that -gnato enables overflow checks as well
Pragma Overflow_Mode (General => Mode, Assersions => Mode);