## Slide 1
Writing a BSP
Notes: <number>

## Slide 2: BSP: Board Support Package
Pre-Ada initialization
  Initialize the processor
  Initialize the board
  Initialize the memory
  Setup an environment for Ada
Board specific environment
  Clock
  Console
  Drivers
Processor support
  Interrupts
  Exceptions

## Slide 3: Pre-Ada Initialization
Purpose: set-up an environment to execute Ada code
  Involve assembly code
  Very processor and board specific, here is an example
  Consult manufacturer documentation
Alternative:
  Use a bootloader/BIOS
  Write your code initialization code

## Slide 4: Pre-Ada Initialization: Reset
Code at reset vector
  In assembly
  Linker script needed to specify the address
  Execute from ROM/Flash
.section ".reset","ax" _reset: b _start_rom .size _reset, . - _reset
ENTRY(_start_rom) … . = 0xfffffffc; .reset : AT (0xfffffffc) { KEEP(*(.reset)) }
Special section
Allocate and Executable
Entry point
Jump to reset code
Size directive
Entry label
Section location

## Slide 5: Pre-Ada Initialization: PLLs, Memory banks, …
PLLs
  Usually at low frequency when powered up
  May have an impact on bus speed
  In assembly
  Execute from ROM/Flash
Memory banks
  Follow the memory map
  Physical addresses
  May require internal logic initialization before
Cache setup
  High impact on performances
MMU setup
  Might be required to declare zone as uncacheable
  On powerpc: use BATs
CPU
  Enable FPU (if any)
…

## Slide 6: Pre-Ada Initialization: Copy to RAM
Initialized data
  To be copied from ROM to RAM
  Usually, several sections (.data, .sdata, .sdata2)
  In linker script, flash address (load addr = lma) /= RAM address (virtual addr = vma)
Cleared data
  No need to copy!
  Known as .bss (and .sbss, .sbss2)
Code
  For performance reasons: RAM accesses are faster than Flash accesses
  Might be needed when programming flash
  Not very different from initialized data
  May require data cache flush / instruction cache invalidation

## Slide 7: Pre-Ada Initialization: Stack initialization
Set the stack pointer
Create an empty frame
You can now call Ada code
lis %r1,__stack_end@h ori %r1,%r1,__stack_end@l
li %r0,0 stwu %r0,-16(1) stw %r0,12(1)
bl main

## Slide 8: Ada Elaboration
Chunks of gnatbind generate file:
procedure adainit; pragma Export (C, adainit, "adainit"); procedure main; pragma Export (C, main, "main");
procedure Ada_Main_Program; pragma Import (Ada, Ada_Main_Program, "_ada_sil4_main"); procedure main is begin adainit; Ada_Main_Program; end;
Elaboration procedure
Entry point
Entry point:
Call elaboration procedure,
Call main subprogram
Import main subprogram

## Slide 9: Calling Ada code before elaboration
It may be easier to write HLL code for pre-initialization
  Loops are easier
  Machine code insertion provide low-level features
But you cannot call an Ada subprogram before its elaboration
  Making it Preelaborate doesn’t always help
Using No_Elaboration_Code restriction helps
  Assure there is no elaboration code
  Like a C unit
pragma Restrictions (No_Elaboration_Code); package P is … end P;